## Slide 1: RBE3002 Final Project
By: Team 3: Clayton “Rhododendron” Dembski, Floris “Grashof” van Rossum and Harry Xie

## Slide 2: Objectives
Navigate the turtlebot3 robot
Produce a map of the environment
Localize using the map
Produce a path using A*
Navigate to a waypoint in the map

## Slide 3: Driving
navToPose()
  rotate()
  driveStraight()
  spinWheels()
Continuous angle adjustment as destination is approached

## Slide 4: Driving
Challenges
  Timing issues
    rospy.get_time()
  Transform issues
    Extrapolation Exception
Improvements
  Driving with curves
  Prevent over and under rotation
  Find a way to prevent or compensate for drift

## Slide 5: Grids
Made Up of Waypoints:
Point
Occupancy value
List of Connected nodes
Currently 4 connected, could be made 8 connected by updating the list of connected nodes.
Each waypoint only connects to unoccupied nodes
Occupancy updates break the two way connection from a waypoint to all connected waypoints

## Slide 6: Grids
Cell Expansion:
From the robot size, the grid spaces are expanded to x by x occupancy grid spaces such that the size is larger than the robot. If the robot were 1.5 cells large
Goes to
100 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 100 | 0
100 | 0
0 | 100

## Slide 7: Grids
Future Improvements:
Set up a Ros Message class to transmit Waypoint objects between Nodes. In this way the robot can better detect how close it may be to a grid and compensate.
Expand only using the initial grid cell size so that there is a smaller likelihood of closing off gaps

## Slide 8: Frontier
Cells that are adjacent to unknown cells but not adjecent to occupied cells
Frontier cells are grouped in clusters based on distance
  Center of the cluster is found
Different frontier cell clusters are ranked
  Distance from robot to cluster center
  Length of the frontier array
Robot keeps navigating until no more frontiers exist

## Slide 9: Frontier

## Slide 10: Path - A*
Determine the best possible path based on cell cost and heuristic
Cell Cost: Manhattan distance to previous cell + cell cost of previous neighboring cell + number of neighboring occupied cells
  Cells closer to walls are avoided
Heuristic: Euclidian Distance to the goal
Performed as expected
Improvements could be made to avoid walls more by weighting cells close to occupied cells more

## Slide 11: Path
Paths next to a 4 connected wall are pushed out to the edge or corner opposite the robot
Has the unintended side effect of smoothing the curve, as 8 connected points are not moved.
Future Improvements:
Better smoothing when away from walls
Reducing drift and slippage
Removing path waypoints when unnecessary